## Slide 2: Introduction
Worked example illustrates both:
  The analysis of a sway frame (ULS)
  The member design check (RHS section)
Analysis of a sway frame:
  Complex problem
  Few guidelines in Eurocode 3
Member check according to EN 1993-1-1
  Method 1 (Annex A)
  Method 2 (Annex B)

## Slide 3: Introduction
Structure of lecture:
  Introduction
  Geometry of the studied frame
  Loading
  Structural analysis
  Column member verification according to Method 1
  Column member verification according to Method 2
  Cross-section check

## Slide 4: Geometry of studied frame
3,
2
m
3,
2
m
3,
2
m
3,
2
m
8
m
8
m
8
m

## Slide 5: Geometry of studied frame
Frame braced out of plane
Treated as two plane frames
Steel S355

## Slide 6: Loading
Load cases:
  Permanent loads
  Wind loading
  3 imposed (variable) loading cases
 | Permanent (vertical) | Variable (vertical) | Wind
Roof level | 17,6 kN/m | 6 kN/m | 6,72 kN
Floor level | 17,6 kN/m | 16,5 kN/m | 13,44 kN

## Slide 7: Loading
Permanent loading (G) Wind loading (W)

## Slide 8: Loading
Imposed loading case 1 (I1) Imposed loading case 2 (I2) Imposed loading case 3 (I3)

## Slide 9: Loading
Frame imperfections:

## Slide 10: Loading
Equivalent horizontal forces: example with load case “G”
To be multiplied with adequate partial safety factor on loads
 | Storey | VEd [kN] | HEd [kN]
G | Roof | 422,4 | 1,11
 | 3rd floor | 422,4 | 1,11
 | 2nd floor | 422,4 | 1,11
 | 1st floor | 422,4 | 1,11

## Slide 11: Loading
Load combinations at ULS:
Load combination
Ultimate limit state
Case 1
1,
.
35
G
+ 1,
.
5
W
Case 2
1,
.
35
G
+ 1,
.
5
I
1
Case 3
1,
.
35
G
+ 1,
.
5
I
2
Case 4
1,
.
35
G
+ 1,
.
5
I
3
Case 5
1,
.
35
G
+ 1,
.
5
W
+ 1,
.
05
I
1
Case 6
1,
.
35
G
+
0,
.
9
W
+ 1,
.
5
I
1
Case 7
1,
.
35
G
+ 1,
.
5
W
+ 1,
.
05
I
2
Case 8
1,
.
35
G
+ 0,
.
9
W
+ 1,
.
5
I
2
Case 9
1,
.
35
G
+ 1,
.
5
W
+ 1,
.
05
I
3
Case 10
1,
.
35
G
+ 0,
.
9
W
+ 1,
.
5
I
3

## Slide 12: Structural analysis
Initial choice for members:

## Slide 13: Structural analysis
Procedure:
  Classify structure (sway here, for illustration)
  As sway, 2nd order effects to be taken into account
  Amplification factors (for each load case)
  “Amplify” bending moments in members
  Check column elements and sections

## Slide 14: Structural analysis
Classification procedure:
  Determine:
  If cr > 10: 2nd order effects are neglected in analysis
  If 3 < cr < 10: approximate method available
  If cr < 3: structure (and load combination) highly sensitive to sway effects, numerical analysis required

## Slide 15: Structural analysis
Example: load combination #5:
Amplification factor:
Load
combination
#
Storey

HEd
[mm]
V
Ed
[kN]
H
Ed
[kN]

cr

cr exact
%

cr

Roof
1,01
721
12
52,57
3
rd
3,37
1707
35
19,34
2
nd
6,03
2694
57
11,32
5
1
st
19,64
3680
80
3,55
3,37
5,4
1,392

## Slide 16: Structural analysis
Amplified internal forces: outer column (LC #5)

## Slide 17: Member checks
Determination of effective length (strong axis):

## Slide 18: Member checks
Determination of effective length (strong axis):

## Slide 19: Member checks
Determination of buckling reduction factor (strong axis):

## Slide 20: Member checks
Determination of buckling reduction factor (weak axis):

## Slide 21: Member checks
Cross-section classification:
Class 1 flanges and Class 2 web
Class 2 cross-section
Plastic resistance allowed for cross-sections

## Slide 22: Plastic resistances
Plastic resistances:

## Slide 23: Member checks: Method 1
Member check according to Method 1:

## Slide 24: Member checks: Method 1
Member check according to Method 1:
  Cm factor: triangular bending moment distribution assumed with My,Ed = 116,25 kNm
  Safe assumption, since the value of the bending moment at top of the member can only decrease since the adjacent beams do not loose their stiffness (due to P- effects) while the column does

## Slide 25: Member checks: Method 1
Member check according to Method 1:

## Slide 26: Member checks: Method 1
Member check according to Method 1:

## Slide 27: Member checks: Method 2
Member check according to Method 2:

## Slide 28: Member checks: Method 2
Member check according to Method 2:

## Slide 29: Member checks: Method 2
Member check according to Method 2:

## Slide 30: Member checks
Remarks:
  Both Methods leads to the same conclusion (safety)
  Major axis checks lead to relatively similar results; however, Method 2 offers more carrying capacity, due to specific interaction factors for hollow sections
  A significant difference is observed for the weak axis check: Method 2 assumes that no interaction between major axis bending and weak axis buckling takes place, unlike Method 1 (moderate influence)

## Slide 31: Cross-section checks
Necessary to check the end sections of the studied member as soon as the “Cm concept” is used
No bending-shear interaction

## Slide 32: Cross-section checks
Necessary to check the end sections of the studied member as soon as the “Cm concept” is used