## Slide 2: Relevant actions
The actions most relevant to building design and the corresponding parts of EN 1991 (EC1) are:
  Part 1-1: Densities, self-weight, imposed loads
  Part 1-3: Snow loads
  Part 1-4: Wind loads
Other relevant parts:
  EN 1990 - Basis of design
  EN 1991 Part 1-2: Actions on structures exposed to fire

## Slide 3: Classification of actions
Actions may be classified according to:
  variation in duration:
    permanent (dead loads)
    variable (imposed, wind, snow)
    accidental (fire, impact)
  spatial variation:
    fixed; free
  nature:
    static; dynamic

## Slide 4: Notation
The following notation is adopted in EC1:
  Dead loads - G
  Imposed loads - Q
  Snow loads - Q
  Wind loads - W
  Accidental loads - A
Suffices inf and sup are used to signify lower and upper bound values respectively

## Slide 5: Dead loads (self weight)
Permanent, fixed action
Calculated on basis of material densities and nominal dimensions
Include allowances for partitions, services...etc as uniformly distributed loads:
  No guidance for calculating values to use
  Estimate based on experience and practice

## Slide 6: Imposed loads
Variable, free action
Characteristic value based on building category (Tables 6.1 and 6.2):
  A - Residential
  B - Office
  C - Assembly areas (5 sub-categories)
  D - Shopping
  E - Storage

## Slide 7: Reductions to imposed loads
Maximum imposed load may not apply simultaneously throughout a building
For beams supporting large areas (A) and columns in multi-storey (n) construction reduction factors  can be applied:
  Beams:
  Columns:

## Slide 8: Snow loads
Characteristic snow load sk based on uniform accumulations on flat ground
sk is determined from national snow maps
Some countries include adjustments for altitude

## Slide 9: Snow load on roofs - s
sk is modified to account for roof form and shape using a shape coefficient i

## Slide 10: Flow chart for calculating snow loads

## Slide 11: Wind loads
The simple procedures below are for structures not susceptible to dynamic excitation
The more thorough treatments in EC1-1-4 should be used for:
  buildings taller than 200 m
  very slender or unusual structures
  temporary structures (lower wind pressures)

## Slide 12: Wind loads
Characteristic wind load wk is based on the reference mean wind pressure qref(0) which depends on the corresponding velocity vref(0)
vref(0) is determined from national wind maps
qref(0) = 0,5·  · vref(0)2
where  is the density of air (= 1,25 kg/m3)

## Slide 13: Terrain category
The reference mean wind pressure qref(0) is modified to account for terrain category (Table 8.1) and height (Figure 8.3)
5 basic categories of terrain are defined:
  Sea, coastal area exposed to the open sea
  Rough open sea, lakes
  Farmland with boundary hedges, small farms, houses
  Suburban, industrial area, permanent forests
  Urban areas

## Slide 14: Terrain category - simplified case
The simple approach described here may be adopted for ‘flat’ terrain
Terrain is ‘flat’ unless close to isolated hills
The exposure coefficient ce(z) can be determined from Figure 8.3 which relates:
  ‘‘reference height’’
  terrain category

## Slide 15: Exposure coefficient ce(z)

## Slide 16: Reference height
3 classes of buildings may be considered
They are defined on the basis of the building height, h, divided by its crosswind width, b:
  Low rise h < b
  Medium rise b < h < 2b
  High rise h > 2b

## Slide 17: Reference height - zones

## Slide 18: Pressure coefficients
The distribution of internal and external pressures on walls and roofs is represented by pressure coefficients
The internal pressure is assumed to be uniform and may be positive (pressure acting outwards) or negative (suction)
The external pressure distribution is non-uniform, and must be determined for each surface

## Slide 19: Internal pressure coefficient
Internal pressure coefficient, cpi, depends on the size and distribution of openings, µ:
Special cases:
  evenly distributed openings in a ‘square’ building
    cpi = 0,25
  ‘closed’ buildings
    cpi = 0,8 or -0,5 (worst case)

## Slide 20: External pressure coefficient
External pressure coefficients cpe must be determined for:
  Each surface
  Two orthogonal wind directions
For walls values of cpe are determined
Values of cpe for roofs depend on the shape

## Slide 21: External pressure coefficients
Obtained for each surface in relation to wind direction:

## Slide 22: Net wind pressures
Internal and external pressures (or suctions) are calculated for each surface as follows:
  External pressure:
  Internal pressure:
Net wind pressure on a surface is the algebraic sum of we and wi

## Slide 23: Load combinations - ULS
Load combinations can be simplified as:
  1,35 Gk + 1,5 Qk
  where Qk is the dominant imposed load &
  1,35 Gk + 1,35 Qk
  where there are more than one imposed loads
Where loads have a beneficial effect:
  0,9 Gk

## Slide 24: Load combinations - SLS
Load combinations can be simplified as:
  1,0 Gk + 1,0 Qk
  where Qk is the dominant imposed load, and
  1,0 Gk + 0,9 Qk
  where there are more than one imposed loads