## Slide 2: Modelling of frames for analysis
Frame components:
  Beams
  Beam-columns
  Joints
Beam
Beam-column
Joint

## Slide 3: Idealisation of 3-D frames
Reduction of 3-D framework to plane frames

## Slide 4: Modelling of frames for analysis
Framing and joints:
  Continuous framing: rigid joint
  Semi-continuous framing: semi-rigid joint
  Simple framing: pinned joint

## Slide 5: Modelling of frames for analysis
The main approaches are:
  Traditional approach in which the joints are considered as (nominally) pinned or rigid
  Semi-rigid approach in which a more realistic model representing the joint behaviour is used. It is usually introduced as a spiral spring at the extremity of the member it attaches (usually the beam)

## Slide 6: Modelling of joints for analysis

## Slide 7: Modelling of lattice girders for analysis
Girder components:
  Chords
  Braces
  Joints
Brace
Chord
Joint

## Slide 8: Modelling of lattice girders for analysis
Framing and joints:
  Simple framing: pinned joints
is usually assumed in the analysis even if the chord members are physically continuous
Secondary moments caused by rotational stiffness of the joints
  They are neglected in the design of joints and members if some geometry conditions specified in Part 1-8 and Lecture 4 are satisfied

## Slide 9: Modelling of lattice girders for analysis
Moments resulting from transverse loads applied between panel points should be taken in the design of the members.
If the above-mentioned geometry conditions are satisfied:
  Braces may be considered as pin-connected to the chords
  Chords may be considered as continuous beams, with simple support at panel joints.

## Slide 10: Modelling of lattice girders for analysis
Detailing of the joints may lead to eccentricities between the axes of the connected members.
These eccentricities result in bending moments in the members and in the joints.
This basically requires to model the joint in a way that allows for this.
  Simplified methods that allow to consider the effects of such eccentricities in the analysis are described in Eurocode 3 Part 1-8

## Slide 11: Modelling of lattice girders for analysis
Moments resulting from eccentricities may be neglected in the design of:
  Tension chord members
  Brace members
They may also be neglected in the design of joints, if the eccentricities are within limits specified on the next slide

## Slide 12: Modelling of lattice girders for analysis
d0 is the diameter of the chord (CHS)
h0 is the depth of the chord in the plane of the girder (RHS)
e is the eccentricity

## Slide 13: Modelling of lattice girders for analysis
Summary table – allowance for bending moments
Type of component | Source of the bending moment |  | 
 | Secondary effects | Transverse loading | Eccentricity
Compression chord | Not if the conditions from Part 1-8 5.1.5(3) specified above are satisfied | Yes | Yes
Tension chord |  |  | No
Brace member |  |  | No
Joint |  |  | Not if the conditions from Part 1-8 5.1.5(5) specified above are satisfied

## Slide 14: Global analysis
Aims of global frame analysis:
  Determine the distribution of the internal forces
  Determine the corresponding deformations
Means:
  Adequate models incorporating assumptions about the behaviour of the structure and its components (members and joints)

## Slide 15: Requirements for analysis
Basic principles to be satisfied:
  Equilibrium throughout the structure
  Compatibility of deformation between the frame components
  Constitutive laws for the frame components
Frame model - element model:
  Must satisfy the basic principles

## Slide 16: Frame behaviour
Displacement
Load
Elastic limit
Peak load
Full elastic response
Load parameter
Displacement parameter

Frame

## Slide 17: Frame behaviour
Actual response of the frame is non linear
Linear behaviour limited
Non-linear behaviour due to:
  Geometrical influence of the actual deformed shape (second order effects)
  Joint behaviour
  Material yielding

## Slide 18: Second order effects
Sway Displacement
Load
Frame

## Slide 19: Second order effects
P -  effect :
  Due to floor sway
  1st order frame stiffness modified
  Dominant effect
P -  effect :
  Due to beam-column deflection
  1st order member stiffness modified
  Significant only for relatively slender members

## Slide 20: Imperfections
Frame imperfection


Member Imperfection
L
N
e
o,d

## Slide 21: Imperfections
Frame imperfection:
  Always to be allowed for
Member imperfection:
  Only for slender members (rare) in sway frames, otherwise it is covered in the relevant buckling curve

## Slide 22: Frame imperfection
The frame imperfection is as follows:
m= number of columns per storey
h= height of the frame

## Slide 23: Frame imperfection
Frame imperfection can be replaced by an equivalent closed system of horizontal forces applied at the floor levels (including the foundation level)
F1
F2

F1

F2

(F1+F2)/2

(F1+F2)/2
Equivalent forces

## Slide 24: Methods of structural analysis
 |  | Material property | 
 |  | Elastic | Plastic
Geometrical effects | 1st order |  | 
 | 2nd order |  | 

## Slide 25: 1st - order elastic analysis
Indefinite linear elastic response of member sections and of joints
Equilibrium established for the undeformed structural configuration
Elastic
Moment rotation characteristic of the section
M
M
M


Moment rotation characteristic of the joint

Elastic
Mj

Mj

## Slide 26: 2nd order elastic analysis
Indefinite linear- elastic response of member sections and joints
Equilibrium established for the deformed structure
Allows for P- effect and, if necessary, for P- effect
Load parameter
2nd order elastic analysis
Displacement parameter

cr

## Slide 27: Rigid-plastic global analysis
Moment rotation characteristics of the joint
Moment rotation characteristics of the member
Mj,Rd
p
Rigid plastic
Mj
Mj,Rd
p
Plastic hinge
Plastic hinge
Mpl.Rd
M
p
Rigid plastic

p
Mpl.Rd
Mpl.Rd
Rigid-plastic member section behaviour
Rigid-plastic joint behaviour when plastic hinges are allowed there

## Slide 28: Rigid-plastic global analysis
Usually a first order analysis
Find critical mechanism
Easy application for simple frames e.g. industrial portal frames
Serviceability deflection check
plastic hinge
location
Load
parameter
Displacement parameter

P,min
Plastic mechanism
Critical collapse load
2
1
3
Beam mechanism
w
W


1
H
A
B
C
D
E

## Slide 29: Rigid-plastic global analysis
Usually a first order analysis
Find critical mechanism
Easy application for simple frames e.g. industrial portal frames
Serviceability deflection check
plastic hinge
location
Combined mechanism
E
W
H


3
A
B
C
D
h
Sway mechanism


2
h
A
B
D
E
H
W
w

## Slide 30: Elastic-perfectly plastic global frame analysis
Elastic-perfectly plastic response of member sections and joints
M

Plastic hinge
M
j,Rd
j
M
Plastic hinge
M
pl,Rd

M
pl,Rd

M
j,Rd


## Slide 31: Elastic-perfectly plastic analysis
2nd-order analysis usually used
Load applied in increments
“Deterioration” of frame stability as plastic hinges form
Load parameter
Displacement parameter
branch 2
1st hinge
elastic buckling load of frame
2nd hinge
elastic buckling load
of deteriorated frame
branch 1
branch 3
branch 4
maximum load