## Slide 2: Introduction
Tension member is subjected to axial tensile force.
Examples of tension members: ‘pin-ended’ members in trusses, lattice girders and bracing members, ( cables, ropes).
Very simple basic design: provision of sufficient cross-sectional area to resist the applied force:
Importance of end connections which often govern the design (when bolted connections).

## Slide 3: Connections
Connections in tubular construction are:
  Very often welded connections with full penetration joints.
  Seldom bolted connections.
When welded connections:
  No weakening of the cross section due to connections.
  Resisting cross-sectional area = gross cross-sectional area.
When bolted connections: detailing affects the tensile member design.

## Slide 4: Bolted connections (1)
Usual to assume uniform stress distribution:
Bolted connection details affect stress distribution:
  Reduction of cross-sectional area at bolt holes.
  Some stress concentration due to bolt holes with peak stresses around the holes.
  Often inevitable small eccentricity in connections resulting in secondary bending.


## Slide 5: Bolted connections (2)
Elastic stress distribution
‘Ideal’ uniform stress distribution
fy
Stress redistribution in the ‘weakened’ cross section made possible because of material ductility.
Use of net cross-sectional area instead of gross cross-sectional area.

## Slide 6: Design resistance of tensile members (welded connections)
Design tension resistance Nt.Rd of members with welded connections:
  Cross-sectional area = gross area A (whole length).
  Reaching yield strength means uniform yielding and further substantial elongation (10 to 15 %).
  Such an elongation is considered unacceptable.
  ULS therefore associated to material yielding.
  ULS does not mean ‘failure’ of the member.
  Design tension resistance:
Recommended value of partial safety factor : M0 = 1,00 (to be specified in National Annex).

## Slide 7: Design resistance of tensile members (bolted connections)(1)
Design resistance of members with bolted connections (non preloaded bolts):
  Cross-section area = gross area A (most of the length).
  Cross-sectional area at connection = net area Anet.
  Reaching yield strength fy in the net area means only slight elongation  not critical at all.
  Reaching yield strength fy in gross area means excessive elongation  ULS type 1  Ductile.
  .
Recommended value of partial safety factor : M0 = 1,00 (to be specified in National Annex).

## Slide 8: Design resistance of tensile members (bolted connections)(2)
  Reaching tensile strength fu in net area means loss of strength and failure  ULS type 2  Brittle.
  Design tension resistance:
Recommended value of partial safety factor: M2 = 1,25, larger than M0 because relative to connection (to be specified in National Annex).
Penalty factor 0,9 to account for unavoidable small eccentricity and still possible stress concentration due to partial redistribution at rupture).

## Slide 9: Additional provisions Category C bolted connections
Fatigue  Preloaded bolts
If, in addition, connections designed to be slip resistant at ULS (Category C connections):
  Stress in the net area limited to yield strength.
  Design resistance of net area:
  Resistance to be in principle compared with force present in the net section (somewhat less than the force in the gross area).

## Slide 10: Additional provisions Requirement for ductility
Special requirement for ductility when, for instance (a) Seismic design (energy dissipation) or (b) Robustness design (substantial elongation without rupture).
  Yielding resistance of gross section required to be less than ultimate resistance of net section.
  Sizing requirement:

## Slide 11: Net area of cross section (1)
Net area = gross area less deductions for fastener holes and other possible openings.
For a single fastener hole:
Deduction = gross cross-sectional area of the hole
When NOT staggered fasteners :
  Total area to be deducted for fastener holes = maximum sum of the cross-sectional areas of the holes in any section perpendicular to member axis.
  Section of maximum sum = critical fracture line.

## Slide 12: Net area of cross section (2)
When staggered fasteners :
  Total area to be deducted for fastener holes = Max of
  a) Deduction for non staggered holes;
  b)
  Section of maximum deduction = critical fracture line
Hole diameter d
Plate thickness t
p
s
s
1,2
2
1
b

## Slide 13: Eccentric connections
Sometimes difficult or even impossible to prevent eccentricity in connections.
Eccentric connections often met where:
  Asymmetrically connected members;
  Asymmetric members (angles, tees, channels).
Eccentricity induces parasitic bending moments.
Bending stresses superimpose stresses due to axial force.
In principle, bending moment reduce the admissible tensile force.

## Slide 14: Eccentric connections
In practice:
  Effects of small eccentricity may generally be disregarded when static loading (plastic redistribution) but to be accounted for when cycling loading (fatigue).
  Effects of significant eccentricity (bending stresses great compared to tensile stresses) to be accounted through:
    Reduced tension resistance in accordance with Chapter on ‘Combined axial force and bending’;
    Design as axially loaded but with a modified net section when angles connected by one leg with single bolt row.
  Account for shear lag see CIDECT Design Guide 3 for )

## Slide 15: Block tearing resistance
Failure line = association of tensile surfaces and shear surfaces.
Consider the probable failure lines and check the design block tearing resistance in each case (see Connections).

## Slide 16: Serviceability, corrosion and fatigue
Tension members transfer load very efficiently with the result of:
  Relatively small cross-sectional areas;
  Susceptibility of ties to significant elongation under axial load (large drift);
  Susceptibility to transverse deflection under self-weight;
  Proneness to vibrations or flutter under wind loading or simply exploitation of the structure.
Light rolled sections are easily damaged in transport.

## Slide 17: Serviceability, corrosion and fatigue
Good practice is to limit the slenderness of tension members:
  No limit values specified in most standards.
  Some recommended values in foreign standards:
    300 for members in buildings and 200 in bridges;
    Sometimes less severe limitations for secondary members (for instance 400 for members in buildings.
Corrosion: consequences of loss of material the greatest for tension members because they are usually relatively highly stressed.

## Slide 18: Concluding remarks
ULS of a tension member is characterised
  by excessive elongation of the member or
  by material failure or separation in possible weakened section.
The design tension resistance of a member with welded connections (full penetration) is given as the design gross cross-sectional resistance.
When bolted connections, account for bolt holes result in the concept of net cross section.

## Slide 19: Concluding remarks
The design tension resistance of a member with bolted connections is taken as the lesser of
  yielding of gross section (ductile) or
  onset of tensile ultimate strength in the net section (brittle).
Where ductile behaviour is required, yielding of gross section should be more determinative than failure in net section.
Small eccentricity in connections may be disregarded when static loading only.
Eccentricity in connections of angles by one leg only may be accounted for by considering a modified net section.

## Slide 20: Concluding remarks
Due attention is paid to shear lag effects in the connections through an appropriate penalty on the net section.
When large eccentricity (eccentric connections) or when eccentricity may not be disregarded, members should be designed as subjected to combined axial force and bending.
Care should be taken of block tearing where necessary.
Serviceability conditions are mainly related to consequences of significant elongation, transverse deflection under self-weight and vibration.
Limit the slenderness of tension members.