## Slide 2: Introduction (1)
This lecture is concerned with compression members (e.g. pin-ended struts) subject to:
  Axial compression only.
  No bending.
Real columns are often end restrained, loaded with accidental eccentricities and sometimes subjected to small transverse loads.
It is distinguished between:
  Stocky columns.
  Slender columns.

## Slide 3: Introduction (2)
Instability phenomenon associated to axially compressed columns is termed ‘column buckling’.
Column buckling may appears in three different ways :
  ‘Flexural buckling’ about one of the principal axis.
  ‘Torsional buckling’ by twisting about the longitudinal axis.
  ‘Torsional-flexural buckling’, which is an interactive buckling involving both above phenomena.

## Slide 4: Introduction (3)
Type of column buckling depends on geometry of the section:
  Flexural buckling: especially for doubly symmetrical sections, such as hot-rolled I and H sections and RHS and CHS.
  Torsional buckling : mostly academic problem.
  Torsional-flexural buckling: especially for open sections where centroid and shear centre do not coincide.
Hollow sections fail normally by flexural buckling  Sole buckling phenomenon covered herein.

## Slide 5: Stocky columns (1)
Characteristics of stocky columns :
  Very low slenderness.
  Unaffected by overall buckling.
  Possibly affected by local buckling.
Compressive resistance of stocky columns:
  A function of the section classification.
  Given by the resistance of the cross-section.

## Slide 6: Stocky columns (2)
Class 1, 2, 3 cross-sections:
  Unaffected by local buckling  Partial safety factor M0.
  Design section resistance = Design ‘plastic section resistance’: Npl,Rd.
  Design compression resistance of the column = Design section resistance :

## Slide 7: Stocky columns (3)
Class 4 cross-sections:
  Local buckling in the elastic range preventing attainment of the squash load  Partial safety factor M1.
  Design section resistance is the ‘local buckling resistance’, i.e. the design plastic resistance of the ‘effective section’ Aeff relative to uniform compression: Neff,pl.Rd.
  Design compression resistance of the column = Design section resistance is:

## Slide 8: Slender columns (1)
Slender columns of ‘high’ slenderness: quasi elastic buckling behavior.
Slender columns of ‘medium’ slenderness: sensitive to imperfections and large interaction between yielding and column buckling.
Elastic Euler ‘critical flexural column buckling load’:
where:
  I : moment of inertia about the bending axis involved.
  Lcr : buckling length, depending on possible restraints.

## Slide 9: Slender columns (2)
Elastic Euler critical buckling stress (flexural buckling):
  where:
  : radius of gyration relative to the bending axis.
  : column slenderness.

## Slide 10: Behaviour of ideal columns (1)
Euler buckling curve
Failure by yielding
Failure by buckling
Euler buckling curve
Lcr/i

Failure by yielding
Failure by buckling

## Slide 11: Behaviour of ideal columns (2)
Euler buckling curve
1
Failure by yielding
Failure by buckling
1
= Relative load
= Relative slenderness

## Slide 12: Behavior of industrial columns
Inelastic buckling occurs prior to Euler buckling load due to:
  Initial out-of-straightness.
  Residual stresses.
  Accidental eccentricity of axial load.
Effects of strain-hardening in low slenderness range.
Lower bound curve resulting from statistical analysis of test results.

## Slide 13: Test results and lower bound
Medium
slenderness
Large
slenderness
Stress
fy
Point of
contra flexure
Slenderness
1
Column buckling curve
= Lower bound

## Slide 14: Effect of imperfections in relation to slenderness
Columns of ‘large’ slenderness:
  Largely unaffected by imperfections.
  Ultimate failure load  Elastic Euler critical load Ncr.
  Carrying capacity independent of the yield stress.
Columns of ‘medium’ slenderness (most columns in practice):
  Affected by both imperfections and material yielding.
  Failure load less than both Euler load and squash load.
  Initial out-of-straightness and residual stresses are the most significant imperfections.

## Slide 15: Residual stresses
Due to differential cooling down during hot-rolling or welding.
Above distribution is typical for hot-rolled section.
Peak residual stress larger (approaching fy) when welded section).
~0,3 fy
compression
tension
compression
~0,2 fy
~0,2 fy

## Slide 16: Residual stresses
Combined with axial stresses cause early yielding.
Flexural stiffness reduced.
=
+
N/A
or =
fy
σN < fy
σn reaching fy

## Slide 17: Initial out-of-straightness eo
Induces bending moments
B
e
e0
N
N

## Slide 18: Initial out-of-straightness eo
If σmax > fy the section becomes partly plastic.
Yielded zone
P
P

## Slide 19: Combined effect of imperfections and axial load
Maximum stress - combination of:
  Bending stress: σB.
  Residual stress: σres.
  Applied axial stress: σ=N/A.
N/A
res
+
B
+
max
=

## Slide 20: Relative slenderness
Concept of ‘relative slenderness’:
βA = 1 for Class 1 - 3 sections.
βA = Aeff /A <1 for Class 4 sections.

## Slide 21: Column buckling curves (1)
Based on experiments:
  More than 1100 tests.
  Hot-rolled sections and hollow sections.
  Range of slenderness ratios between 55 and 160.
Supported by numerical investigations.
Buckling resistance obtained as a reduction factor  applied to the section resistance A A fy
‘Reduction factor’  is related to the relative slenderness .
Buckling curve: f )

## Slide 22: Column buckling curves (2)
Initial out-of-straightness:
  Shape: Similar to first bucking mode, i.e. half sine-wave.
  Magnitude: L/1000 as substantiated by measurements.
Residual stresses related to section type and drawn from measurements.
Five basic curves relative respectively to some cross-section types and characterized by specific values of imperfection factor 

## Slide 23: Column buckling curves (3)

## Slide 24: Column buckling curves (4)
Analytical expression of buckling curves:

## Slide 25: Imperfection factor 
Imperfection factor depends on:
  Shape of column cross-section.
  Axis of buckling (y or z axis).
  Fabrication process (hot-rolled, welded or cold-formed).
  Massiveness measured as h/b (for hot-rolled).
Buckling curve a0 | a | b | c | d
Imperfection factor 0,13 | 0,21 | 0,34 | 0,49 | 0,76

## Slide 26: Selection of an appropriate buckling curve
Cross-section type | Fabrication | Buckling about axis | Buckling curve | 
 |  |  | S235 S460  S420 | 
Hollow sections | Hot-finished | any | a | a0
 | Cold-formed |  | c | c

## Slide 27: Design steps (1)
Determination of ‘buckling lengths’ Lcr,y and Lcr,z relative to flexural buckling about respectively y and z axis, based on:
  Length between restraints.
  Connection details producing end restraints.
Select a steel grade and deduce yield strength for appropriate thickness fy.
Select a hollow section based on rough preliminary design or design experience.
Determine section properties : A, Iy, Iz and A.

## Slide 28: Design steps (2)
Calculate the ‘characteristic’ section resistance:
NRk = AAfy
Calculate the elastic ‘critical loads’:
Deduce ‘relative slenderness’:

## Slide 29: Design steps (3)
Keep the larger relative slenderness (only applicable to hollow sections!):
Select appropriate buckling curve based on:
  Forming process.
  Steel grade.
Adopt the value of the ‘imperfection factor’ associated to this curve.
Calculate the ‘reduction factor’:

## Slide 30: Design steps (4)
Calculate the ‘design buckling resistance’ of the column:
Design check:
  If Nb,Rd > NEd : Design acceptable.
  If Nb.Rd < NEd : Design unacceptable / Requirement for resizing.

## Slide 31: Concluding summary (1)
Column buckling = Instability of axially loaded compression members.
Column buckling may occur by: a) flexural buckling, b) torsional buckling or c) torsional-flexural buckling
Due to their high torsional properties, hollow sections are mostly concerned with flexural buckling only.
Flexural column buckling may occur by bending about anyone of the principal axes of the cross-section.
For each direction of possible buckling, a column buckling length must be determined.
Stocky columns are unaffected by column buckling but may be affected by local plate buckling.

## Slide 32: Concluding summary (2)
Resistance of stocky column = Squash load, i.e. plastic axial resistance of gross cross-section (Class 1, 2, 3 sections) or effective cross-section (Class 4 sections).
Slender columns with high slenderness fail mostly by elastic buckling.
Slender columns with medium slenderness are the most sensitive to the effects of imperfections and fail by inelastic buckling.
Resistance of slender column is lower than both the squash load and the elastic critical buckling load; it is assessed based on column buckling curves.

## Slide 33: Concluding summary (3)
Appropriate column buckling curve is selected based on the forming process – hot finished or cold formed – and the steel grade.
Entering this curve with the relative slenderness provides the corresponding reduction factor.
Reduction factor used as a ‘knock-down’ factor to be applied on the section resistance to get the buckling resistance.
Check of the buckling resistance to be conducted for both possible directions of buckling.