## Slide 2: Background
10 Structural Eurocodes developed for CEN.
4 are directly relevant to steelwork:
  EC 0 - Structural safety, Combination of actions.
  EC 1 - Actions (loads).
  EC 3 - Steel structures.
  EC 4 - Composite structures.
Intended to establish consistent and harmonized standards throughout Europe.
Aimed at favoring cross-border interactions and enabling wider fair competition.

## Slide 3: Background
Step 1: Pre-standard ENV
+ NAD (National Application Document).
Step 2: Standard EN + National Annex
= Registered national standard (alternative to regular national standard).
Present state of development :
All the EN available.
Finalisation of the National Annexes.

## Slide 4: Structure of EC’s
EC’s are published in parts, divided into:
  Chapters and Appendices
    Sections {N.n}
      Clauses {N.n.n}
        Sub clauses {N.n.n.n}
        • Paragraphs {N.n.n.n.(p)}
Distinction is made between:
  “Principles (P)” which must be obeyed (no alternative).
  “Application rules” which follow the principles but alternative methods are allowed.

## Slide 5: General Eurocodes
EN 1990 - Basis of structural design (EC 0).
EN 1991 - Actions on structures (EC 1):
    Part 1: General actions:
    1.1 Densities, self-weight and imposed loads.
    1.2 Actions on structures exposed to fire.
    1.3 Snow loads.
    1.4 Wind actions.
    1.5 Thermal actions.
    1.6 Actions during execution.
    1.7 Accidental actions.
    Part 2: Traffic loads on bridges.
    Part 3: Actions induced by cranes and machinery.
    Part 4: Silos and tanks.
EN 1090 - Execution of steel structures.

## Slide 6: Eurocode 3: EN 1993 Steel Structures
EC 3 - Design of steel structures
  Part 1-1: General Rules and rules for buildings
  Part 1-2: Fire resistance
  Part 1-3: Supplementary rules for cold-formed members and sheeting
  Part 1-4: Supplementary rules for stainless steels
  Part 1-5: Plated structural elements
  Part 1-6: Strength/Stability of shell structures
  Part 1-7: Planar plated structures subject to out of plane loading
  Part 1-8: Design of joints
  Part 1-9: Fatigue
  Part 1-10: Material toughness and through-thickness properties
  Part 1-11: Design of structures with tension components
  Part 1-12: High strength steels

## Slide 7: Eurocode 3: EN 1993 Steel Structures
EC 3 - Design of steel structures (cont.)
  Part 2: Steel bridges
  Part 3: (3.1) Towers, masts, and (3.2) Chimneys
  Part 4: (4.1) Silos, (4.2) Tanks and (4.3) Pipelines
  Part 5: Piling
  Part 6: Crane supporting structures

## Slide 8: Eurocode 4: EN 1994 Composite Structures
EC 4 - Design of composite steel and concrete structures
  Part 1-1: General Rules and rules for buildings
  Part 1-2: General rules - Structural fire design
  Part 2: General rules and rules for bridges

## Slide 9: Eurocodes for steel products
EN 10025, EN 10133 and EN 10164:
Hot-rolled sections.
EN 10210 and EN 10219:
  Hollow sections.

## Slide 10: Design approach of ECs
Based on limit state design philosophy.
Principal limit states for steel structures:
  Ultimate Limit States (ULS), concerned with carrying capacity and overall equilibrium:
    Resistance : Yielding, buckling, formation of mechanism, overturning.
    Material fatigue and brittle fracture.
  Serviceability limit state (SLS), concerned with ‘function’:
    Deflection.
    Vibration.
Three design situations: (a) normal, (b) transient, (c) accidental.

## Slide 11: Limit state design principles
Define relevant limit states.
Determine appropriate actions for each limit state in consideration.
Analyze using appropriate methods and structural models accounting for variability of parameters to determine:
  Design effects {E}.
  Design resistance {R}.
Ensure no limit state is exceeded: {R > E}.

## Slide 12: Characteristic and design values
‘Characteristic’ values for data are typical rather than safe.
‘Design’ values should be used to check limit state condition: {E < R}.
Partial safety factors are applied to characteristic values to obtain design values.
Suffices k and d are used to mean ‘characteristic’ and ‘design’ values respectively.

## Slide 13: Partial (safety) factors
Partial (safety) factors  are applied to characteristic values for both actions (F) and resistance model (M) to account for variability.
The value of  depends on:
  The limit state under consideration.
  The variable to which it is applied.
  The context - e.g. is an action beneficial in relation to the considered effect.

## Slide 14: Variability of actions
Precision of modeling actions varies:
  Dead loads related to material density and thickness.
  Imposed loads based on type of occupancy.
  Wind and snow loads based on meteorological data.
Probability of load combinations varies (additional combination factors ).
Values of partial (safety) factors reflect these differences.

## Slide 15: Variability of material and section properties
Resistance is related principally to material and section geometry.
Yield strength and ultimate tensile strength of steel are ‘minimum guaranteed’ values, and therefore taken as ‘characteristic’ values.
Other properties, notably Young’s modulus, shear modulus and Poisson’s ratio are much less variable.
Variations in section geometry are accounted for by partial safety factors used elsewhere.

## Slide 16: Ultimate Limit States
The following conditions should be considered:
  Loss of static equilibrium.
  Exhaustion of resistance under static loadings because of excessive deformation, formation of mechanism, rupture, loss of stability.
  Fatigue under repeated loadings.

## Slide 17: Serviceability Limit State
The following conditions may need to be considered:
  Excessive deformations or deflections, affecting adversely appearance or causing damage to non structural elements or to supported finishes.
  Excessive vibrations causing discomfort or damage or limiting functional effectiveness.
Both conditions are associated with stiffness rather than strength.
For most buildings, providing stiffness to control deflections normally limit vibrations too.

## Slide 18: Concluding remarks
EC = Harmonized European standards.
10 structural EC’s : Structured documents with principles and application rules.
Only some EC’s relevant to steelwork.
Based on limit state philosophy : ULS  ‘carrying capacity’ and SLS  ’functionality’.
EC + National Annex = Registered national code.
Choices or parameter values let free in EC fixed in National Annexes.