## Slide 2: Introduction
Beam is the basic structural component.
Many section shapes and beams types may be used for that purpose depending on the magnitude of loading and the span.
Hollow sections used as beams or components of lattice girders.
Hollow sections have a large torsional rigidity.

## Slide 3: Design of beams
Steel beams can often be designed on the basis of bending moment resistance by:
  Ensuring the design moment resistance of the selected cross-section exceeds the maximum applied moment,
and checked for stiffness by:
  Ensuring the beam does not deflect so much that it affects serviceability considerations.

## Slide 4: Section classification Maximum slenderness ratios
Element | Class 1 | Class 2 | Class 3
Flange | c/tf ≤ 9ε | c/tf ≤ 10ε | c/tf ≤ 14ε
Web subject to bending | d/tW ≤ 72ε | d/tW ≤ 83ε | d/tW ≤ 124ε
Web subject to compression | d/tW ≤ 33ε | d/tW ≤ 38ε | d/tW ≤ 42ε
c
d
c
d

## Slide 5: Evolution of the direct stress distribution
(a)
Elastic
(b)
First
yield
(c)
Elastic
plastic
(e)
Strain
hardening
(d)
Fully
plastic
Strain
distribution
Stress distribution at several stages of loading
Class 1 or 2
Mpl,Rd
Class 3 (full section)
Class 4 (effective section for bending)
Mel,Rd

## Slide 6: Moment resistance (1)
Class 1 and 2 cross-sections:
  Moment resistance = design plastic resistance moment:
Class 3 cross-sections:
  Moment resistance = design elastic resistance moment:
The recommendedvalue ofthe partial safety factor is M0 = 1,0; to be fixed in National Annexes.
Wel is elastic section modulus of the section.

## Slide 7: Moment resistance (2)
Class 4 cross-sections:
  Moment resistance = design elastic resistance moment (due account for local buckling):
Weff is elastic section modulus of the ‘effective’ section for bending.

## Slide 8: To be or not to be… … Restrained (1)
Beams which are unable to move laterally are termed "restrained"
Unaffected by out-of-plane buckling
(lateral-torsional instability)

## Slide 9: To be or not to be… … Restrained (2)
Beams may be considered restrained if:
  Full lateral restraint is provided by positive attachment of a floor system to the top flange of a simply supported beam (Many designers consider the friction generated between a concrete slab and steel beam to constitute a positive attachment).
  Adequate torsional restraint of the compression flange is provided, for example by profiled roof sheeting.
  Closely spaced bracing elements are provided such that the minor axis slenderness is low.
  Sections bent about their minor axis cannot fail by lateral torsional instability and it is unlikely that sections with high torsional and lateral stiffness (e.g. RHS) will fail in this way.
It is the designer's responsibility to make structural details consistent with above assumption.

## Slide 10: Bending resistance of ‘restrained’ beam (1)
Simply supported span: ULS is fulfilled when the design value of the bending moment MEd is not greater than the bending section resistance Mc,Rd:
MEd ≤ Mc,Rd
Mc,Rd depends on the section shape, material strength and section classification (see earlier).

## Slide 11: Bending resistance of ‘restrained’ beam (2)
Fastener holes in the tension flange may be ignored if tensile flange area such that (ductile resistance):
Fastener holes in the tension flange need not be allowed for provided above limit is fulfilled when applied to the whole tension zone of the cross-section.
Fastener holes in the compression zone of the cross-section may be ignored unless oversized or slotted holes.

## Slide 12: Shear resistance (1)
When plastic design (in absence of shear buckling, i.e. h/t ≤ 72/:
  Shear only
VEd ≤ Vc,Rd
with:
If shear buckling:
Vc,Rd = Vb,Rd (see Part 1-5)
but normally hollow sections are not concerned

## Slide 13: Shear resistance (2)
  Shear area Av for hollow sections

## Slide 14: Shear resistance (3)
  Combined shear force and torque moment:
VEd ≤ Vpl,T,Rd
with:
When elastic design, at most critical point for shear:
Design shear stress (constant over the wall thickness) due to torque moment

## Slide 15: Resistance to combined bending and shear
In any generality, resistance to combined bending and shear requires:
MEd ≤ MV,Rd
When plastic design:
  When VEd ≤ 0,5 Vpl,Rd: MV,Rd = Mc,Rd
  When VEd > 0,5 Vpl,Rd: MV,Rd = M’c,Rd (fy’)
    where fy’ = (1-) fy
    and
When elastic design: von Mises criterion to be fulfilled at the most critical point.

## Slide 16: Resistance of unrestrained beam (1)
Proneness to lateral torsional buckling:
Check:

## Slide 17: Resistance of unrestrained beam (2)
Lateral torsional buckling resistance:
Wy = Wpl,y for Class 1 and 2 cross-sections;
Wy = Wel,y for Class 3 cross-sections;
Wy = Weff,y for Class 4 cross-sections.
Determination of beam slenderness:
where:
Effect of moment distribution

## Slide 18: Resistance of unrestrained beam (3)
Determination of reduction factor LT:
where:

## Slide 19: Resistance of unrestrained beam (4)
Selection of imperfection factor LT:
Cross-section | Limits | Buckling curve
Rolled sections | h / b ≤ 2 | a
 | h / b > 2 | b
Welded sections | h / b ≤ 2 | c
 | h / b > 2 | d
Other sections | / | d

## Slide 20: Resistance of unrestrained beam (5)
Limiting L/(h-t) ratios preventing lateral-torsional buckling (approximate):
Lateral torsional buckling disregarded for
when beams in buildings and no further account of end restraints.

## Slide 21: Serviceability
Deflections and vibrations must be limited to avoid:
  Adverse affects to the appearance.
  Impaired use of the structure.
  Discomfort to the occupants.
  Damage to the finishes and contents of a building.
Acceptable limits for deflections should be agreed between the client, designer and competent authorities
For guidance EN 1990 gives recommended limiting values for vertical deflections

## Slide 22: Vertical deflection limits
Flat roofs are vulnerable to ponding.
Necessary to check roof deflections carefully including allowances for construction inaccuracies, settlements of foundations, deflection of roof materials, etc.
 | Limits | 
 | δmax | δ2
Roofs generally | L/200 | L/250
Roofs frequently carrying personnel | L/250 | L/300
Floors generally | L/250 | L/300
Floors and roofs supporting plaster | L/250 | L/350
Floors supporting columns | L/400 | L/500

## Slide 23: Vertical deflection limits
Important to ensure that oscillation and vibrations are not so great that they cause discomfort to users
Floors in dwellings and offices:
  Lowest natural frequency > 3 cycles/second
Floors in gymnasia/discos, ..:
  Lowest natural frequency > 5 cycles/second

## Slide 24: Summary
The main design requirement for restrained beams is the provision of adequate bending strength
Design moment resistances for cross-sections depend upon section classification
Holes in the tension zone of a beam may in some cases cause a reduction in the moment resistance
Co-existent shear forces below 50% of the plastic shear resistance do not affect moment resistance
Where high shear forces occur, the contribution of the shear area to moment resistance should be deducted
Serviceability limits on deflection or vibration may control the design