## Slide 2: Design process
Architectural
requirements
Execution
considerations
Conception
Preliminary
design
Design checks
Environmental considerations
Actions
Analysis
ULS
SLS

## Slide 3: Global frame analysis
Aim : Determination of internal forces and moments.
Several options with increasing sophistication:
  Elastic or plastic global analysis.
  First order or second order global analysis.

## Slide 4: Allowance for imperfections
Two types of imperfections:
  Structural imperfections: residual stresses.
  Geometric imperfections:
    Frame imperfections: initial out-of-plumb of the columns.
    Member imperfections: initial out-of-straightness.

## Slide 5: Modelling of imperfections (1)
Structural imperfections:
  Consist in residual stresses.
  Direct modelling too complex for practice purposes.
  Alternative indirect modelling by magnifying the geometric imperfection of the compression members.
  Modelling required in all circumstances.

## Slide 6: Modelling of imperfections (2)
Frame imperfections:
  Direct modelling as out-of-plumb depending on:
    Reference initial slope on the vertical direction.
    Number of bays.
    Number of storeys.
  Alternative indirect modelling by substituting above out-of-plumb by equivalent horizontal forces at the levels of the storeys (to be considered in addition to the external loads).
  Modelling required in all circumstances with the result that the effects are taken into account in the loading side of the design checks. .

## Slide 7: Modelling of imperfections (3)
(Compression) member imperfections:
  Direct modelling as initial out-of-straightness (covering also the effects of residual stresses) the magnitude of which is a proportion of the system length.
  Alternative indirect modelling by substituting above out-of-straightness by equivalent uniformly distributed transverse forces (to be considered in addition to the external loads).
  Modelling required in specific but are circumstances.
  Mostly no need in practice but effects then taken into account in the resistance side of the design checks.

## Slide 8: Frame/Member imperfections

## Slide 9: Elastic or plastic global analysis
Elastic global analysis:
  No requirement for any ductile behaviour.
  Permitted in all circumstances.
  Practised in the past and still today.
Plastic global analysis:
  Large demand in rotation capacity (ductility).
  Never required in any circumstance.
  Prior requirements on steel properties, joint properties, cross-section shape and cross-section classification.
  Possibility of making SLS more determinative than ULS.
Elastic global analysis recommended

## Slide 10: First order or second order elastic global
First order elastic global analysis:
  Equilibrium with reference to the initial configuration.
  Permitted when second order effects sufficiently small.
Second order elastic global analysis:
  Equilibrium with reference to the deflected configuration.
  Due allowance made for second order effects.
  Two ways:
    Actual second order elastic global analysis.
    Second order effects assessed approximately and reflected through magnification of results of first order elastic analysis.
Criterion : Classification as sway/non sway frame.

## Slide 11: Frame classification as sway or non sway
Classification criterion:
Not an intrinsic frame property as depending on the load combination in consideration.

## Slide 12: Elastic global analysis of non sway frames
Non sway  Second order effects negligible
First order elastic global analysis is permitted.
Member resistance (instability) based on buckling lengths associated to non sway buckling mode.
Conservatively system lengths may be taken as buckling lengths.

## Slide 13: Elastic global analysis of sway frames
Second order analysis required when cr < 3.
Simplified method: Amplified sway moment method (ASMM) permitted when cr ≥ 3:
  First order analysis under gravity loads.
  First order analysis under horizontal loads.
  Amplification of the results of step 2) by
  Superimposition of results of steps 1) and 3).
  Member resistance (instability) with buckling lengths associated to non sway buckling mode of the frame.

## Slide 14: Elastic global analysis of sway frames
Simplified method: Sway Mode Buckling Length Method (SMBL) permitted without restriction:.
  First order analysis under all the loads.
  Use the results of step 1) for checking the member resistance (instability) with buckling lengths associated to sway buckling mode of the frame.
Account for P- effects with SMBL more erratic than with ASMM  ASMM recommended.

## Slide 15: Implications for design of the choice of the global analysis
Share of efforts between tasks
Simplification of global analysis
Sophistication of global analysis
Global analysis
ULS design checks
Overall Design Task = Analysis + Design Checks

## Slide 16: Implications for design of the choice of the global analysis
The more sophisticated the analysis tool employed, the less are the design check tasks following analysis.

## Slide 18: Summary (1)
Frame design consists in global frame analysis followed by a series of design checks.
Due account shall be made of frame and member imperfections, where necessary.
There are still some reasons for recommending the practice of elastic global analysis.
To which extent consideration of so-called second order effects (P- effects) is required depends on the frame classification as sway or non sway.
The classification as sway or non sway is relative to the load combination in consideration.

## Slide 19: Summary (2)
For non sway frames, the P- effects are negligible so that first order analysis suffices.
For sway frames, the P- effects need to be accounted for either by performing a second order analysis or by using simplified approaches referring to first order analysis and indirect approximate account for P- effects.
The most sophisticated the method of global analysis, the less the number and sophistication of the design checks still to be conducted.