## Slide 2: Structure of EC3
Compared to ENV version (single document), present EC3 has been substantially reorganised and implemented (12 Parts: 1-1 to 1-12).
Part 1-1 of EC3 is the master document.
Part 1-1 of EC3 (EN 1993-1-1) contains of 7 Chapters and 4 Annexes.
Present course covers all topics of EC3 Part 1-1 and some additional material (especially design of joints, fatigue, ….).
Annexes are generally not referred to directly.

## Slide 3: Structure of EC3 Part 1-1
Chapter 1 General
Chapter 2 Basis of design
Chapter 3 Materials
Chapter 4 Durability
Chapter 5 Structural analysis
Chapter 6 Ultimate limit states
Chapter 7 Serviceability limit states
Annexes A, B, AB and BB (informative)
Definitive status to be given in National Annex.

## Slide 4: Terminology and symbols
Eurocodes use precise terminology and symbols.
Terminology:
  Global analysis
  Frame and Sub-frame
  Type of framing
  Lengths related to stability
Symbols:
  General nature, section and material properties
  Extensive use of suffices (possibly in sequence)

## Slide 5: Special terms in EC3
General:
  Frame = Assembly of connected structural elements.
  Sub-frame = Part of frame used for global analysis.
Type of framing:
  Simple : joints not resisting bending moments.
  Continuous : joints assumed to be rigid.
  Semi-continuous : connection characteristics needing explicit consideration in global analysis.
Lengths relating to member stability:
  System length: length between lateral restraints/ends.
  Buckling length: equivalent pin-ended system length.

## Slide 6: Special terms (EC3 Part 1-8 : Joints)
Partial strength joint: design resistance of joint less than design resistance of connected member.
Simple joint (pinned) : joint not capable of transmitting significant bending moments.
Rigid (continuous) joint: only structural properties of members (and not of joints) need explicit consideration in global analysis.
Semi-rigid (semi-continuous) joint: structural properties of both members and joints need explicit consideration in global analysis.

## Slide 7: Special terms (EC3 Part 1-8 : Joints)
Partial strength joint: design resistance of joint less than design resistance of connected member.
Full strength joint: design resistance of joint at least equal than design resistance of connected member.

## Slide 8: Special terms in EC3 (analysis)
Braced frame: sway resisted by a sufficiently stiff bracing system.
Unbraced frame: inadequate sway resistance provided by the bracing system.
Sway frames: poor lateral stiffness  need for consideration of effects of horizontal displacements.
Non-sway frame: large lateral stiffness  no need for consideration of effects of horizontal displacements.

## Slide 9: Material properties (1)
Five nominal grades of steel (EN 10 025):
  S235 nominal yield strength = 235 N/mm2
  S275 nominal yield strength = 275 N/mm2
  S355 nominal yield strength = 355 N/mm2
  S420 nominal yield strength = 420 N/mm2
  S460 nominal yield strength = 460 N/mm2
Strength reduced for elements of higher thickness : see product standards or simplified table in EN 1993-1-1.
Grade S690 covered in EC3 Part 1-12 (HSS).

## Slide 10: Material properties (2)
For all structural steels:
  E = 210 000 N/mm2
   = 0,3
   = 1210-6 1/°K
Material requirements for ductility (global plastic analysis).
General guidance on material requirements for:
  Fracture toughness.
  Through-thickness properties.
{See details in
EC3 Part 1-10}

## Slide 11: Global structural analysis (1)
Method should be consistent with design assumptions.
Possible need for consideration of joint behaviour  Joint modelling for global analysis.
Types of global analysis:
  Elastic analysis : only stiffness of members and (possibly joints) are concerned.
  Plastic analysis: both stiffness, strength and ductility of member sections and (possibly) joints are concerned.

## Slide 12: Global structural analysis (2)
Accuracy of global analysis:
  First order : equilibrium in non deformed geometry.
  Account for second order effects:
    Second order analysis: iterative process with equilibrium in deformed geometry  no more application of principle of superposition.
    Corrections for second order effects superimposed to results of first order analysis  still application of principle of superposition.
  Criterion for required consideration of second order effects.

## Slide 13: Global structural analysis (3)
Account of imperfections for global analysis:
  Frame (global) imperfections:
    Lack of verticality of columns.
    Required in any circumstance.
    Modelling or substitution by equivalent horizontal nodal loads.
  Member (local) imperfections:
    Lack of straightness of member axis.
    Required (criterion given) in few rare circumstances.
    If required: Modelling or substitution by equivalent transverse distributed loads.
    If not required: Implicit account through member stability check formulae.

## Slide 14: Design checks at ULS (1)
Check under factored loads (static conditions) or fatigue loads (fatigue conditions).
Internal forces in individual elements determined by global analysis.
Elements normally designed and checked as isolated components.
Design checks depend on :
  Type of member.
  Type of global analysis (see next slide).

## Slide 15: Design checks at ULS (2)
Total design task = Global analysis + Design checks
Decrease in complexity of global analysis
Increase in complexity of global analysis
Global analysis
Checks at ULS
Share of efforts

## Slide 16: Design checks at ULS (3)
Frames must be checked for:
  Resistance of cross-sections: plastic or elastic depending on class.
  Resistance of members: including member and frame stability.
  Resistance of joints : see EC3 Part 1-8.
Tension members need only be checked for :
  Resistance of cross-sections.
Fatigue resistance when required:
  See EC3 Part 1-9.

## Slide 17: Design checks at SLS (1)
Checks for service loads (non factored).
Main design criteria at SLS:
  Deflections (horizontal and vertical).
  Vibrations.
Deflections and vibrations usually determined based on:
  Elastic global analysis.
  Bare frame structure ( without floors, roof, partitions, cladding, …).

## Slide 18: Design checks at SLS (2)
Deflections:
  Calculated values seldom meaningful (for several reasons) but used as an index of stiffness.
  Excessive deflections impair appearance and/or cause local damage in supported elements.
  Need for consideration of pre-camber when present.
  Consider permanent and variable loads separately.
  Limit values for vertical deflections of beams and horizontal deflections frames : recommended in EC 0 but to be specified in National Annex.
  Limiting deflection  adequate stiffness.

## Slide 19: Design checks at SLS (3)
Dynamic effects from:
  Machinery.
  Self-induced vibrations.
Resonance when close natural frequencies of structure and source of excitation respectively.
Excessive vibration = Source of discomfort.
Limit values for vibration of floors: recommended in EC 0 but to be specified in National Annex.
Possible sophisticated check by dynamic analysis.

## Slide 20: Concluding remarks
EC 3/EC 4 dedicated to steel/composite structures.
EC 3 comprises 12 parts.
EC 3 Part 1-1 is the ‘master document’.
EC 3 Part 1-1:
  Is composed of 7 chapters and 4 annexes.
  Uses (as other parts) precise terminology and symbols.
  Covers steel grades up to S460.
  Includes general on structural global analysis.
  Describes the design checks at both ULS and SLS.